## Slide 1: NOC (NETWORK OPERATION CENTRE)

## Slide 2: Introduction to NOC
“A Network Operations Center (NOC) is an organizational unit that Handles day-to-day monitoring of the Infrastructure and Serves as a single point of contact for customers, internal and external Creates, processes, and resolves events that arise in the network”
A network operations center (NOC) is a place from which administrators supervise, monitor and maintain a telecommunications network. Large enterprises with large networks as well as large network service providers typically have a network operations center, a room containing visualizations of the network or networks that are being monitored, workstations at which the detailed status of the network can be seen, and the necessary software to manage the networks.

## Slide 3: NOC Benefits (Why NOC is IMP in today’s organizations?)
Greater Network or Infrastructure Visibility
Optimize operational expenses and/or enhance efficiency.
Monitoring and Managing services
Providing End-to-End Managed Services Solutions.
High Availability and maximum up time
Operate in shifts for 24x7x365 days format for remotely monitoring and managing the Enterprise Infrastructure.
Escalation policy is followed to deal with alerts of different severity.

## Slide 4: 4 Essential area
Knowledge Base
Reporting and Measurements
Monitoring/ Ticketing System
IT Process automation

## Slide 5
Knowledge base
Keep one centralized source for all knowledge and documentation that is accessible to your entire team. This knowledge base should be a fluid information source, so make sure you continuously update it with experiences and lessons learned for future reference and improvements
Reporting and Performance Analysis
Create reports on a daily and monthly basis. A daily report should include all major incidents of the past 24 hours and a root cause for every resolved incident. This report is useful and essential for the shift leaders and NOC managers.
It also keeps the rest of the IT department informed about the NOC activities and of major incidents. Compiling the daily reports into a monthly report will help measure the team’s progress. It will also show areas where improvements can be made or indicate any positive or negative trends in performance.

## Slide 6
Monitoring
Infrastructure monitoring, which can consist of the servers, the network or the data center environment.
Depending on organization need and their size, the various monitoring are being used:
Network Monitoring: HP NNMi, WhatsUpGold, Netflow Scrutinizer, Solarwinds, etc
Application Monitoring: Appneta, SiteScope, HP BPM, etc.
Server/DC Monitoring : SCOM, SiteScope, Nagios, etc.
Ticketing tools: ServiceNow, BMC Remedy, HPSM, etc.

## Slide 7
IT Process Integration:
IT Process Integration can save significant time on repetitive, daily tasks, and frees up time for more strategic projects.
IT process Integration, also known as run book automation (RBA),is the automation of an IT task through the orchestration and integration of tools, people and process through a single workflow.
IT Process Integration also helps reducing mean time to recovery (MTTR) in case of critical incidents.
For example, specific workflows can be triggered during off hours for handling critical system events.
Examples : password reset, disk space clean-up, restart services etc...

## Slide 8: NOC Processes
What are the operational, structured processes that you should implement for effective and repeatable results? Here are our top ones.
Escalation: 1] Verical Escalation
2]Functional Escalation
Prioritization: URGENCY x IMPACT
Incident Handling: Analyze, logging, categorize, follow up till closure
Conclusion: RCA part, Closure notes.

## Slide 9: Knowledge & skills
By ‘knowledge and skills’ we don’t mean the obvious technical knowledge and network ‘know-how’ your team members must hold to run day-to-day operations, but rather – How you can ensure your team’s skills are used to their best potential, and how to keep those skills up to date over time
Clearly defined roles: Tasks & responsibilities
Communication & Collaboration
NOC employee training

## Slide 10
Tasks & responsibilities:
Why does it matter ?
Mostly because it affects decisions making. Without clearly defined roles and responsibilities, disagreements between operators lead to late decisions and actions, or to no decisions taken at all. This can affect customers, critical business services, and urgent requests during off hours.
A shift manager should be responsible for: prioritizing tasks, assigning work to operators based on their skills, verifying that tickets are opened properly and that relevant personnel are notified when required, escalating problems, communicating with management during important NOC events, sending notifications to the entire organization, preparing reports, and making critical decisions that impact many services, such as shutting down the data center in case of an emergency.
Operators, on the other hand, should be responsible for handling the technical aspect of incidents – either independently or by escalating to another team member with the required skills. Operators are also responsible for following up and keeping tickets up to date.

## Slide 11
Communication & Collaboration:
Encourage and promote collaboration :
If the NOC team is geographically spread out or is located in different countries, you should spend even more efforts on communication and collaboration, to overcome cultural and language barriers.
Define NOC members as focal points :
NOC members act as focal points for important IT areas, such as NT, UNIX, Network, or a specific project. These members attend the meetings of the relevant teams, deliver new information and knowledge to the rest of the NOC, and handle specific professional challenges
Attending the meetings:
Make sure a member of the NOC attends weekly change management meetings and communicate issues or upcoming activities, such as planned downtime, to the rest of the team.

## Slide 12
NOC employee training :
A new NOC operator may not know where to find a procedure or how to execute it, or in a more severe case - take a decision that causes equipment damage or results in critical downtime.
Make sure to put in place an extensive training program for new NOC employees.
Make sure experienced NOC members, preferably shift leaders, train new employees. Update the training program on an ongoing basis, and make sure it includes topics such as required users and permissions, known problems, troubleshooting, teams and important contacts

## Slide 13
THANK YOU